## Slide 1
CAN (MCP2561)
BMS-OK RELAY (+LED)
Current Sense 1
bq76PL455A
(Slave)
FAULT_N
WAKEUP
UART_TX
P014 – EPWM1A
P002 – GIOA[0]
P005 – GIOA[1]
P039 - SCITX
P009 – GIOA[2]
AIR SENSE (+LED)
P083 – AD1IN[8]/ADIN2[8]
UART_RX
P038 - SCIRX
TMS5701224
P090 – DCAN1RX (J10_38)
P089 – DCAN1TX (J10_39)
TX
RX
P016 – EPWM1B
P022 – EPWM2A
P025 – EPWM2B
P140 – EPWM6A
P141 – EPWM6B
P032 – EPWM4A
P095 – MIBSPI1CLK
P093 – MIBSPI1SIMO
P094 – MIBSPI1SOMI
P126 – GIOB[0]
TM4C129ENCPDT
JTAG:
P108 – P113
5v
1MHz
P118 – N2HET1[10]
P106 – N2HET1[8]
P033 – N2HET1[7]
P036 – N2HET1[4]
P006 – N2HET1[11]
P024 – N2HET1[3]
P035 – N2HET1[9]
P041 – N2HET1[15]
P125 – N2HET1[14]
P031 – N2HET1[5]
P124 – N2HET1[12]
P023 – N2HET1[1]
P030 – N2HET1[2]
P139 – N2HET1[16]
JTAG Header
JTAG Header
JTAG
USB
USB Header
Follow Design from Dev Board
FAULT_N
WAKEUP
UART_RX
UART_TX
Galvanically isolated level shifter 5V (slave) to 3.3V (Master) (see datasheet for recommended use)
ISOW7842DWE
Tacho Feedback
14 PWM controlled 12V Fans
http://www.formfactors
.org/developer/specs/
REV1_2_Public.pdf
2x Fan PWM in
2x Fan PWM in
2x Fan PWM in
2x Fan PWM in
2x Fan PWM in
2x Fan PWM in
2x Fan PWM in
Fan Tacho out
Fan Tacho out
Fan Tacho out
Fan Tacho out
Fan Tacho out
Fan Tacho out
Fan Tacho out
Fan Tacho out
Fan Tacho out
Fan Tacho out
Fan Tacho out
Fan Tacho out
Fan Tacho out
Fan Tacho out
Group traces by fan connector
P131 – LINRX
P132 – LINTX
UART_TX
UART_RX
3.3v
P105 – MIBSPI1NCS[0]
SD Card
http://elm-chan.org/docs/mmc/mmc_e.html
DO
DI
SCLK
CS
P070 – AD1IN[9]/ADIN2[9]
P072 – AD1IN[10]/ADIN2[10]
Ambient Temperature Thermistor 1
P075 – AD1IN[11]/ADIN2[11]
Current Sense 2
Ambient Temperature Thermistor 2
For connector position on board talk to Aaron C. or Jake C.
Reset Circuit
RST_OUT
RST:
Warm + Cold
PWR
GND
PWR
2 pin connector from auxiliary contactor, use pullup.
Check with Tom D. with CAN circuit design
MASTER PCB
5V to 3.3v & 1.2v PSU
(see dev PCB for design)
5V and GLV from Power PCB
12V from Power PCB
Pull-up: CS, MOSI, MISO
Pull-down: CLK -------------------------------->>> Check site^ for details
MOSFETs with Pull-ups
Put MOSFETs near connectors
7 Seg Hex Display
LED Driver (STP08CP05MTR)
SDI
CLK
LE
P130 – MIBSPI1NCS[1]
0 resistor links

## Slide 2: Master PCB Components
Name | Description | Quantity | Manufacturer | Link | Part number
Connectors (communications) | IDC type (2.54 or 1.27mm pitch if needed for space) | ? |  |  | 
Connectors (Fans) | Fan 4 pin header | 14 | Molex or Generic |  | 
Fan | Static pressure 80x80x25mm max 4 wire with 25kHz PWM control | 14 per pack | MEGAFAN | http://uk.farnell.com/ebm-papst/8412n-2ghp/fan-pwm-control-80mm-12vdc/dp/1875270 Range: https://goo.gl/3ni9tn | 8412N/2GHP
Bidirectional Level shifter |  | 12 | NXP | http://uk.farnell.com/nxp/gtl2003pw-118/ic-level-translator-8-i-p-tssop/dp/2400477 | 
Galvanically isolated level shifter | Digital Isolators High-Efficiency, Low-Emissions, Reinforced Digital Isolator With Integrated Power 16-SOIC -40 to 125 | 1 | TI | https://www.mouser.co.uk/ProductDetail/Texas-Instruments/ISOW7842DWE/?qs=sGAEpiMZZMssyD0wnx%2fymBptqwsKUoFZB4eOkTZIrnbkaqiP9XAw8A%3d%3d | ISOW7842DWE